OPERATION INSTRUCTIONS

To “Start” the Lift in “AUTO” mode:

- POWER UP LIFT

- CLEAR ALL E-STOPS

- PRESS “SYSTEM START”

- PRESS “MODE SELECT”

- SELECT “AUTO” AND PRESS “ENTER” THEN PRESS “ESC”

- PRESS “LIFT START”

- THE LIFT WILL START RUNNING WHEN IT RECEIVES “PERMISSION TO RUN” FROM THE CUSTOMER.

To “Stop” the Lift in “AUTO” mode:

- NON-EMERGENCY - PRESS “LIFT STOP”

- EMERGENCY - PRESS “E-STOP”

##### TO ENTER “MANUAL” mode:

- STOP THE LIFT

- PRESS “MODE SELECT”

- SELECT “MANUAL” AND PRESS ENTER THEN PRESS “ESC”

##### TO run the lift backward/FORWARD:

###### STOP THE LIFt

  - CLEAR ALL FAULTS

  - PRESS “MODE SELECT”

  - SELECT “RUN LIFT BACKWARDS” PRESS ENTER THEN “1” AND ENTER TO SELECT BACKWARD OR “0” AND ENTER TO SELECT FORWARD THEN PRESS “ESC”

## TO JOG LIFT:

## Enter “MANUAL” MODE

- SELECT DIRECTION PRESS “JOG SELECT” (SELECT REVERSE OR FORWARD AND PRESS “ENTER” THEN PRESS “ESC”)

- PRESS “JOG LIFT”

##### TO CLEAR ANY FAULT:

- FIX THE FAULT AS IDENTIFIED ON THE DISPLAY

- PRESS “FAULT RESET” (PRESS “ESC” IF NECESSARY)

- ABOVE ALL, FOLLOW DIRECTIONS ON THE DISPLAY