OPERATION INSTRUCTIONS

To “Start” the Lift in “AUTO” mode:

- POWER UP LIFT

- CLEAR ALL E-STOPS

- PRESS “SYSTEM START”

- PRESS “MODE SELECT”

- SELECT “AUTO” AND PRESS “ENTER”

- PRESS “LIFT START”

- THE LIFT WILL START RUNNING WHEN IT RECEIVES “PERMISSION TO RUN” FROM THE CUSTOMER.

To “Stop” the Lift in “AUTO” mode:

- NON-EMERGENCY PRESS “LIFT STOP”

- EMERGENCY PRESS “E-STOP”

##### TO ENTER “MANUAL” mode:

- STOP THE LIFT

- CLEAR ALL FAULTS

- PRESS “MODE SELECT”

- SELECT “MANUAL” AND PRESS ENTER

## TO JOG LIFT:

## Enter “MANUAL” MODE

- SELECT DIRECTION PRESS “JOG SELECT” (SELECT REVERSE OR FORWARD AND PRESS ENTER)

- PRESS “JOG LIFT”

##### TO CLEAR ANY FAULT:

- FIX THE FAULT AS IDENTIFIED ON THE DISPLAY

- TO CLEAR A LOAD FAULT, “JOG LIFT” MUST BE HELD UNTIL THE LIFT STOPS ITSELF.

- PRESS “FAULT RESET” (PRESS “ESC” IF NECESSARY)

##### TO VIEW LIFT STATISTICS:

- RUN THE LIFT IN “AUTO” MODE

- PRESS AND HOLD “SYSTEM START”

##### ABOVE ALL, FOLLOW DIRECTIONS ON THE DISPLAY