SETUP INSTRUCTIONS

To LOGIN TO LIFT:

- STOP THE LIFT IN MANUAL MODE

- PRESS THE LOGIN BUTTON

- PRESS THE ENTER BUTTON

- ENTER ‘XXX’ AND PRESS ENTER *Call TKF for Password*

- PRESS ESC

- PRESS THE NUMBER ‘5’ FIVE TIMES

- YOU ARE NOW ABLE TO ENTER THE VALUES FROM THE MA01.DWG

THERE ARE  (8) VALUES THAT NEED TO BE ENTERED ONCE THE PROGRAM IS IN THE SETUP SCREEN.

- THE TKF JOB NUMBER USUALLY THE FIRST FOUR DIGITS OF

DRAWING NUMBER. (A109MA01…THE JOB# IS A109)

- THE LIFTS FEET PER MINUTE (FPM) WHICH IS SHOWN ON THE

MA01 DRAWING. THIS VALUE SHOULD BE ROUNDED UP TO THE NEAREST WHOLE NUMBER. 100.5 FPM SHOULD BE ENTERED AS 101 FPM.

- THE PLATFORM LENGTH IN INCHES. WHICH IS SHOWN ON THE

MA01 DRAWING.

- THE MAX BOX LENGTH IN INCHES. WHICH IS SHOWN ON THE

MA01 DRAWING.

- THE LIFTS LOADS PER MINUTE (LPM). WHICH IS SHOWN ON THE MA01 DRAWING. THIS VALUE SHOULD BE ROUNDED UP TO THE NEAREST WHOLE NUMBER. 35.5 LPM SHOULD BE ENTERED AS 36 LPM.

- IF THE LIFT IS DESIGNED WITH A LUBRICATOR OR NOT. THE CHOICES ARE (1) = TRUE OR (0) = FALSE. TYPICALLY THE ANSWER WILL BE (0), MOST LIFTS DO NOT HAVE THIS OPTION.

- IF A LUBRICATOR IS PRESENT, THE INTERVAL IT SHOULD  BE ACTIVE IN HOURS (HOURS BETWEEN ‘ON’ TIME). IF A LUBRICATOR IS  PRESENT THIS NUMBER IS TYPICALLY DETERMINED BY THE CUSTOMER. A NORMAL VALUE COULD BE 12 HOURS DEPENDING ON RATE AND HEIGHT OF THE LIFT.

- IF THE LIFT IS DESIGNED WITH A DISCHARGE MOTOR STARTER THAT IS CONTROLLED BY OUR PROCESSOR OR NOT. THE CHOICES ARE (1) = TRUE OR (0) = FALSE. TYPICALLY THE ANSWER WILL BE (0), MOST LIFTS DO NOT HAVE THIS OPTION.

ONCE ALL EIGHT PARAMETERS HAVE BEEN ENTERED CORRECTLY, PRESS ‘ESC’ TO EXIT THE SETUP MODE. THE LIFT SHOULD BE READY FOR NORMAL OPERATION. PLEASE NOTE THESE PARAMETERS ARE FACTORY SET BY TKF AND CHECKED FOR PROPER FUNCTION. IT IS IMPERATIVE THAT THE INFORMATION BE ENTERED CORRECTLY. INACCURATE INFORMATION WILL MOST DEFINITELY RESULT IN POOR LIFT PERFORMANCE AND POSSIBLE DAMAGE. IF ANY INFORMATION IS UNCLEAR OR NOT UNDERSTOOD AT THE TIME OF SETUP, PLEASE CONTACT THE TKF ENGINEERING DEPARTMENT FOR FURTHER ASSISTANCE.